ESA 422/485

SERIAL RS 422/485 CARD

The RS-422 / 485 Serial Card provides two fully programmable RS 422 / 485 serial ports. RS 422 / 485 Interface enables more reliable communication over longer distances than is possible with RS-232C Interface.

- Two Independent RS-422 / 485 serial ports

- Reliable communication upto 1.2 Km (4000 feet)

- Programmable Baud rate of upto 56,000

- Two or four wire operation.

- The Serial Ports can be configured either as COM1 / COM2 or COM3 / COM4 and would then be directly accessible from DOS.

## COMPARISON OF RS232, RS422 AND RS485

| DESCRIPTION | RS-232 | RS-422 | RS-485 |
| --- | --- | --- | --- |
| NO. OF DRIVERS | 1 | 1 | 32 |
| NO. OF RECEIVERS | 1 | 10 | 32 |
| TRANSMISSION DISTANCE SPEED | 15M. 20kBIT/SEC | 12M, 10 MBIT / SEC; 120M, 1M BIT / SEC; 1.2KM, 100KBIT / SEC; | 12M, 10 MBIT / SEC; 120M, 1M BIT / SEC; 1.2KM, 100KBIT / SEC; |
| INTERFACE TYPE | SINGLE ENDED | DIFFERENTIAL | DIFFERENTIAL |