PARALLEL TO SERIALCONVERTER

A PRINTER SUPPORT PRODUCT

ESA Parallel to Serial Converter converts Centronics parallel input data to RS 232 C serial output data. Selection of all standard output bauds between 150 to 19200 and data formats is done through jumper change-overs on the PCB.

SPECIFICATIONS:

| Power Supply | : | 9V AC, 300mA (Suitable power adapter supplied) |
| --- | --- | --- |
| Input | : | Centronics Parallel (TTL) |
| Output | : | Serial (RS 232 C) |
| Data Format | : | 5,6,7 or 8 bits.1,1 1/2 or 2 stop bits; even, odd or no parity; supplied with 7 data bits, 1 stop bit and parity even. |
| Baud | : | 150, 300, 600, 1200, 2400, 4800, 9600, or 19200; Supplied with 9600 baud. |
| Communication Mode | : | DTE (Data Terminal Equipment) ie., serial data is transmitted on pin 2 of 25 pin - 'D' type connector. |
| Hardware Handshake | : | Hardware handshake is provided through pins 5 and 6 of serial output connector. A low (-12V) on either input stops output; These inputs may be connected to printer DTR output or any other such control signals. |
| Power on Indication | : | LED |
| Input Connector | : | 25 pin 'D' type male (compatible to PC parallel printer output; suitable cable for PC connection is supplied). |
| Output Connector | : | 25 pin 'D' type male. |