SERIAL TO PARALLEL CONVERTER

A PRINTER SUPPORT PRODUCT

ESA Serial to Parallel Converter converts RS 232 C input data to Centronics standard parallel output data. Selection of all standard input bauds between 150 to 19200 and data formats is done through jumper change-overs on the PCB.

SPECIFICATIONS:

| Power Supply | : | 9V AC, 300mA |
| --- | --- | --- |
| Input | : | Serial (RS 232 C) |
| Output | : | Centronics Parallel(TTL) |
| Data Format | : | 5,6,7 or 8 bits.1,1 1/2 or 2 stop bits; even, odd or no parity; supplied with 7 data bits, 1 stop bit and parity even. |
| Baud | : | 150, 300, 600, 1200, 2400, 4800, 9600, or 19200; Supplied with 9600 baud. |
| Communication Mode | : | DTE (Data Terminal Equipment )ie., serial data is received on pin 3 of 25 pin - 'D' type connector. |
| Hardware Handshake | : | Hardware handshake ouput is provided through pins 4 and 20 of serial input connector. A low(-12V) on these outputs indicates that the serial input to the converter should be stopped. These outputs may be connected to inputs CTS and DSR or any other such control inputs of the sending device. |
| Power on Indication | : | Green LED |
| Error Indication | : | Red LED indicators error condition due to one or more of the following. 1. Parity error, 2. Framing error, 3. Overrun error. |
| Input Connector | : | 25 pin 'D' type male |
| Output Connector | : | 25 pin 'D' type female (similar to PC printer adapter output connector) compatible with the standard PC cable to centronics parallel printer. |