ESA  RS 485 <-> RS  232 C

Electro Systems Associates Pvt. Ltd. (ESA) manufactures various types of Microprocessor Trainers, In-Circuit Emulators, EPROM Programmers, PC Add-on cards and Printer Support Products (PSP) which can be used for various purpose like manpower development, Research and development, instrumentation etc., One such converter is ESA RS 485 <-> 232. ESA RS 485 <-> 232 converter is a bi-directional interface having features of Multidrop, simplex and point to point communication.

MAIN FEATURES:

- Non power, power stealing from the interface

- Drivers maintain high impedance when power off

- Asynchronus full duplex mode

- Dual drivers and dual receivers

- Data rate up to 100kBps at 4000 feet

- Connectors RS 232(25 pin female), RS 485 (9 pin male or 8 pin connector)

- Can drive up to 32 drivers on the bus.

#### Note:   optional power adapter available for longer distance

The converter can be used as both two wired or four wired RS 485 multidrop (master slave) network. Supports hardware handshake signals ( DSR & DTR ) in point to point half / full duplex communication . This converter provides the flexibility for equipment / systems which have RS485 but should communicate with RS232 port. One can have an a facility of Multidrop and long cable distance (4000 feet) although they have only RS232 Interface in their equipment / system. Two Computers having RS 232 Serial Port can communicate between them for longer distnce (4000 feet ) using two RS 485<->232.

CONNECTOR DETAILS:

| 25 PIN FEMALE (J1) | 9 PIN MALE (J3) | 8 PIN BERG CONNECTOR (J4) |
| --- | --- | --- |
| 2 TXD | 1 TX- | 1 TX+ |
| 3 RXD | 2 TX+ | 2 TX- |
| 4 RTS | 4 RX+ | 3DTR+ |
| 5 CTS | 5RX- | 4DTR- |
| 6 DSR | 6DTR- | 5DSR+ |
| 20 DTR | 7DTR+ | 6DSR- |
|  | 8DSR+ | 7RX+ |
|  | 9DSR- | 8RX- |